## Slide 1: NuttX RTOS CAN Bus Driver for Espressif ESP32C3
Faculty of Electrical Engineering
Jan Charvát
Supervisor – Ing. Pavel Píša, PhD.
16.6.2022

## Slide 2: Introduction
NuttX CAN subsystem analysis on ESP32C3
Implementation of CAN (TWAI) driver
Testing and demonstration of driver functionality
Notes: Espressif uses Two Wire Automotive Interface because of trademark, configurable GPIO

## Slide 3: ESP32C3 DevKit
RISC-V single-core
microcontroller
Wi-Fi & Bluetooth 5 (LE) module
SJA1000 CAN 2.0 controller
Notes: Advantages- cheap, many GPIOs & peripherals, frequency 160 MHz, public lighting of the city of Milan, using SJA1000 opencore
Red rectangle TWAI and 2,3 pins mapped CAN

## Slide 4: NuttX CAN subsystem
Open-source RTOS
Character Device Driver
“lower” half driver
Notes: Higher – Generic part, Lower – architecture-specific – my implementation, comparison with SocketCAN, but in NuttX mostly implemented character device driver, also it has better performance on small chips
Shorter – SocketCAN or Character Device Driver – say HW dependent and HW independent

## Slide 5: Related work
ESP-IDF TWAI
  Official Espressif framework
LinCAN
  SJA1000 support
  Thorough bit timing solutions
NXP lpc17-40 CAN
  NuttX CAN implementation
Notes: LinCAN bit timing later used in SocketCAN
For the beginning I use ESP IDF for functionality test and then as inspiration
LinCAN for Linux – inspiration for bit timing in SocketCAN

## Slide 6: TWAI initialization
Power and clock
enabled,
pins configuration
Reset TWAI device – different register layout
  Error counters, Bit timing
  Acceptance filters
Setup interrupts
Notes: After system boot, 13 DATA registers
RESET – for parameter setting is changed controller to RESET mode and it changes possibility to modify some registers and change 13 DATA registers

## Slide 7: TWAI Transmission
Single TX buffer
Upper driver holds SW TX FIFO
Modes for transmission
  Loopback mode
  Standard mode
Support for extended IDs
Notes: Go straightforward to point – low level controller writes to DATA registers, two modes, self reception and standard regime

## Slide 8: TWAI Reception
RX interrupts
RX buffer – first received frame mapped on DATA registers
Support for extended IDs
Notes: Controller receives to HW FIFO and informs to data received by interrupts

## Slide 9: Testing
Bit timing
Linux CAN utils
Latency Tester
  Timing Analysis of a Linux-Based CAN-to-CAN Gateway
  Matěj Vasilevski contribution
Motor control application in pysimCoder
Notes: Verified bit timing on oscilloscope, next was against implementation of CAN on system on Linux and proper testing with latency tester
Colleague works on contribution to Latency tester

## Slide 10
Linux CAN utils

## Slide 11
Latency Tester
Notes: Channel both-directinal, different ID for higher priority

## Slide 12
Motor control in pysimCoder
Notes: Experiment with pysimCoder and data transfer is visible

## Slide 13: Conclusion
Driver integration completed
TWAI (CAN) support has been added to NuttX mainline
  https://github.com/apache/incubator-nuttx/pull/6005
  At Espressif Alan C. Assis ported to Xtensa ESP32
Successful demonstration of functionality
Future work
  Implement rest of IOCTL calls
  Restore from overflow
Notes: In normal use no RX overflow occurs, but in simulated RX overflow I tried implementation depending on manual, but it does not work
Pull request

## Slide 14: Thank you for your attention
Faculty of Electrical Engineering
Jan Charvát
16.6.2022

## Slide 15
Notes: Illustrative example